## Slide 1: Net Metering & Distributed Generation in PNM Territory
PNM PRAC Net Metering Workshop
May 12, 2026
Jason Hoyle, Director of Research, EQ Research LLC
On behalf of the Renewable Energy Industries Association of New Mexico

## Slide 2: Introduction
EQ Research
https://eq-research.com/
Renewable Energy Industries Association of New Mexico (REIA-NM) https://reia-nm.org/
2
Notes: EQ: 50-state regulatory and legislative tracking, plus IRP, GRC, EV, Data Center, etc.
REIA-NM: Supports, promotes, and accelerates the just and orderly transition to renewable energy in New Mexico.

## Slide 3
Disclaimer
The material in this presentation was prepared without advance knowledge of the content of PNM’s net metering presentation or details of PNM’s current inclinations towards possible changes to net metering, and the lack of inclusion of any particular subject does not imply support. Information contained herein is for discussion purposes only.
3

## Slide 4: PNM Roadmap to Default TOD
*Slide 2, PNM Presentation, 1/20/2026; **Slide 3, PNM Presentation, 3/31/2026
Roadmap Component* | Net Metering/DER Proposals**
Residential TOD pilot rate | Force Net Metering and legacy TOU customers onto Pilot TOD rate by default for duration of pilot
Flatten Energy Blocks in Res. 1A rate | Remove highest-price block and increase price in the consolidated energy block for use of ≥ 451 kWh/month
Distributed Generation | Eliminate banking (i.e., kWh carried forward from month to month) of excess generation
4

## Slide 5: Residential TOD Pilot Rate
DG Proposal
Force Net Metering customers onto Pilot TOD rate by default for duration of pilot1
General Concerns
Efficacy: available pilot results show limited impact on actual peak load and higher bills for most participants
Limited data: Pilot design is exploratory and not based on robust data
Customer Differentiation & Distribution: Limited controls for EVs and total energy use
Net Metering & DER
Net Metering and DER customers are a “very small percentage” of pilot participants and not included in analysis of pilot2
Discriminatory treatment
  Customers shall be billed for service in accordance with the rate structure and monthly charges that the customer would be assigned if the customer had not interconnected a qualifying facility. – NMAC 17.9.570.14 (C)(1)
  PURPA regulations contain similar provisions prohibiting discrimination in the rates for sales to a Qualifying Facility - 18 CFR Part 292
1. Slide 3, PNM Presentation, 3/31/2026; 2. Analysis Memo, p. 1, 3/31/2026 PRAC
5

## Slide 6: Residential TOD Pilot Rate
Source: Figure 2-1, Time-of-Day (TOD) Pilot Impact Analysis – 2025 Results, 3/31/2026 PRAC
Pilot results show evidence of load-shifting, but very little actual reduction in peak load
About 2/3 of pilot participants had higher bills: +13% in Summer, +7% in Winter1
The 1/3 w/ benefits started with bills about 3x higher than other participants and saved $42,371, while the other 2/3 paid $19,814 more2
1. Slide 9, PNM Presentation, 8/19/2025; 2. Slide 23, PNM Presentation, 8/19/2025
Net Metering/DG capacity (325 MWAC) is 15.19% of peak load1 and w/ storage could reduce peak load by that amount or more
The current TOD pilot rate design rewards the highest-use customers and penalizes customers who use less energy
Consider…
6

## Slide 7: Flatten Energy Blocks in Res. 1A Rate
DG Proposal
Consolidate two highest-price energy blocks into a single block at higher price1
General Concerns
Price: Increases price in second block, which is 150 kWh for average customer
Incentive: Encourages higher energy use by highest-use customers by reducing marginal cost of highest-kWh block
Equity Impact: Penalizes customers that use the least energy and rewards customers using the most energy
Net Metering & DER
Penalizes the average customer and net metering/DER customers by increasing monthly bills without a change in purchases
Interacts with 3rd Proposal to discourage new net metering/DER adoption and compounds other incentive reductions
  Reduces the value of net monthly excess generation carry-forwards – to utility and all customers
  Will increase recent decline3 in adoption of net metering and DER technology and incentivize new adopters to provide less support to the grid
1. Slide 3, PNM Presentation, 3/31/2026; 2. Analysis Memo, p. 1, 3/31/2026 PRAC; 3. Slide22, PNM Presentation, 8/19/2025 – new interconnections in 2024 and H1 2025 are the lowest since at least 2019
7

## Slide 8: Flattening Inclining Block Rate
“Revenue requirement doesn’t change, but the amount of revenue to be collected within each seasonal rate bucket changes, thus altering rates.” – Slide 11, Presentation, Jan. 20, 2026
“Due to the relative economics between the current inclining 1A rate structure and the TOD, potential savings are highly correlated (93%) with monthly usage and not necessarily with how customers are using power (i.e., on-peak vs. off-peak)” – Slide 13, Presentation, Jan. 20, 2026
“Flattening the blocks can address the inequities caused by the inclining block rates, so that all customers experience the same economic incentives” – Slide 20, Presentation, Jan. 20, 2026
Meter Reading & Billing & Collection per-Customer Costs
2019 rate case: $5.02/bill, $27,654,858 (40%)
2024 rate case: $10.45/bill, $62,565,190 (51%)
– Slide 20, Presentation, Jan. 20, 2026
600 kWh/Month (average customer*)
+4.9% Summer & +3.5% Non-Summer months
Increased bills for 55.1% of non-LI customers & 62.5% of low-income customers** and likely for many net metering customers
1200 kWh/Month Bills
+0.1% Summer months
-1.43% Non-Summer months
Source: Slide 18 data, PNM Presentation, 3/31/2026; *2024 GRC Application, p. 3; **Slide 28, Presentation, 8/19/2025
8

## Slide 9: Distributed Generation
DG Proposal
Eliminate banking, i.e. kWh of excess generation carried forward from month to month1
General Concerns
Existing Net Metering: Undermines value of existing Net Metering investments
Contrary to Grid Mod Purpose: Reduces DG and renewables and increases emissions2
Higher Costs: Increases direct costs to ratepayers, lowers value of Grid Mod investments, and creates economic costs
Net Metering & DER
Stops kWh exports in high-output months from offsetting kWh imports in low-output months
Reduces value of Net Metering/DER
  Discourages new net metering/DER adoption and compounds incentive reductions, e.g. federal tax credit
  Reduces the value of net monthly excess generation carry-forwards – to utility and all customers
Increases costs to all ratepayers
  ↑ sales = ↑ RPS compliance cost
  ↓ utility working capital = ↑ cost of capital
  Opportunity & Economic Costs, incl. reduced jobs and local spending, missed technology benefits, higher emissions costs, and encourages less grid support from customers
1. Slide 3, PNM Presentation, 3/31/2026; 2. NM Stat § 62-8-13 (2025);
9

## Slide 10: Banking Excess kWh is Valuable to PNM
19.5% of net metering customers “banked” more than an average customer’s annual usage by June 2025 and 10% were “super exporters”1
Many banked kWh exports are no-cost kWh that PNM sells at full retail value
As of Q1 2024, 71.85 million kWh were “banked”2 and I estimate more than 90 million by Q1 2025
Banked kWh from net metering between Q1 2021 and Q1 2025 have provided PNM shareholders and ratepayers with over $41 million in no-cost working capital
Slide 22 data, Presentation, 1/20/2026;
Slide 25, Presentation, 8/19/2025;
Net Metering Transaction: kWh exports are sold at retail when exported, that revenue is re-invested repeatedly and compounds until a pay-out or the kWh offsets a customer import.
Chart: Capital Contribution of Banked RECs (Q1 YYYY)
| 2021 Q1 | 2022 Q1 | 2023 Q1 | 2024 Q1 | est. 2025 Q1
kWh | 30598325 | 44144756 | 56220026 | 71849999 | 91409156
Value$ | 3059832.5 | 4628663.875 | 9434218.1212 | 19884301.811 | 41553423.1487
10

## Slide 11: Other Issues
Will PNM attempt to claim net metering/DG RECs without compensation?
Storage is not generation and the addition of storage does not increase a systems capacity for the 10 kW threshold (17.9.570.14 NMAC & 17.9.570.15 NMAC), Broadview Solar
DER Aggregation – FERC Order 2222 – and Virtual Power Plants support Grid Mod statute purposes
Many examples of successful & effective utility-facilitated DER programs nationally
DERs in New Mexico
2,141 solar jobs in 2024; #12 state per capita1
As of March 2026, ranked #17 in solar capacity and #5 in storage capacity2
$6.8 billion total solar investment2 (not including direct, indirect, or induced economic benefits)
DER technology adds as much value as utilities encourage them to add
1. National Solar Jobs Census 2024; 2. SEIA State Overview;
11

## Slide 12: Cost-Benefit Analysis & Reasonableness Do the requested Grid Mod investments, incentives, programs and expenditures “improve the public utility's electrical system efficiency, reliability, resilience and security; maintain reasonable operations, maintenance and ratepayer costs; and meet energy demands through a flexible, diversified and distributed energy portfolio, including energy standards established in Section 62-16-4 NMSA 1978[?]” - New Mexico PRC, 22-00058-UT, Order at pp. 9-10, 5/31/2023

## Slide 13: Thank You! Questions?
Jason Hoyle
jhoyle@eq-research.com